## Slide 1: PowerWalk (“pwalk”) A High-Speed, Portable, Multi-Threaded Tree-Walk Utility *** Limited Distribution ***
Version 2.09 – January, 2020
Bob Sneed
Isilon Corporate Advisory Engineer
Dell EMC | Unstructured Data Division
Email: Bob.Sneed@Dell.com

## Slide 2: Disclaimers
The software described herein is FREE CODE provided for instructional purposes only. It is not an official or supported product of Dell Technologies, Dell EMC, or any of its affiliates. Neither Dell Technologies nor Dell EMC assume any liability whatsoever for any use of this software or derivatives of this software, including any potential consequential damages which could arise from its use.
The C source code includes this disclaimer ...
  // This is FREE CODE. There are no warranties,
  // express or implied, of any sort whatsoever,
  // including any warrantees of correctness or
  // suitability for any particular purpose.
This project is a work-in-process. All aspects of its features and implementation details are subject to change without notice.
Notes: Caveat User.

## Slide 3: Outline
General Discussion & Usage
pwalk Generic Modes
pwalk Platform-specific Modes
pwalk Options
Operational Notes

## Slide 4: General Discussion & Usage

## Slide 5: Motivations
Performance
  Little’s Law: X=N/R
    Throughput (X) = Concurrency (N) / Response Time (R)
    When R cannot be lowered, increase N to increase X
  Treewalk speed is governed by the latency of directory lookups and file attribute lookups
  In turn, those operations are governed by the latency of NAS protocol (NFS or SMB) namespace RPCs (LOOKUP, READDIR, READIRPLUS, GETATTR, etc)
  All NAS operations inherit network latency
  OneFS NAS namespace and metadata operations are relatively slower without SSD metadata acceleration
  On OneFS, multiple nodes can be leveraged to improve scaling with concurrency
Portability
  Coded in relatively portable C for Linux, OSX, Solaris, or native OneFS deployment
Extensibility
  Designed to enable rapid delivery of tactical functionality
Notes: Ease-of-use is not a primary design goal, but tends to improve over time!

## Slide 6: Git it here …
https://github.com/WhizBob/pwalk
  src/ - Mostly-portable C code (OneFS, Linux, Mac OS, Solaris) plus various platform-dependent Makefiles
  doc/ - Word & Powerpoint documentation, plus Excel permissions spreadsheet
  bin/ - Prebuilt binaries (bin/<platform>) - not guaranteed to match the current code!

## Slide 7: Compile and Build
Mostly portable C code
  80% monolithic pwalk.c C code
  Uses POSIX pThreads for concurrency
  pwalk_acls.[ch] for ACL-handling (Linux only)
  Uses Python symbiont code for –audit (OneFS only)
Simple compile & link
  OSX: Makefile.osx
  Linux: Makefile.linux
  OneFS: Makefile.onefs7 | Makefile.onefs8
  Solaris: Makefile.solaris
  Windows: Theoretically possible …
    See also: https://sourceware.org/pthreads-win32/
Notes: pwalk a fairly straightforward C code, with the main extra consideration being inclusion of the pThreads library (the POSIX portable threads library).
The O’Reilly book is all one needs to get started with pThreads.

## Slide 8: pwalk Design
Main control thread Argument processing Thread Management Event Logging Statistics Aggregation & Reporting
Worker thread #1
Worker thread #2
…
Worker thread #N
Stay in Lane
Maintain Speed
Single multi-threaded process
One main control thread
N concurrent worker threads (-dop=N)
Each worker threads scans a single directory at a time which it pops from the FIFO. Discovered directories are pushed to the FIFO as they are encountered
pwalk.fifo
pwalk.log
.log
.log
.log
worker_N.<type>

## Slide 9: pwalk Usage - Intro
Usage: pwalk [<primary_mode>] [<secondary_mode> …] [<option> ...] [<directory> ...]
Each pwalk invocation must specify …
  At most one <primary_mode> value
  Zero or more <secondary_mode> values
  At least one <primary_mode> or <secondary_mode>
  Zero or more <option> values (these may vary depending on the modes selected)
  Zero or more <directory> values (default is just ‘.’)
Many <option> values can be passed to pwalk via the pwalk parameter file, which is specifed by ‘-pfile=<filename>’
<directory> arguments must consistently either be relative pathnames (relative to the –source= or [source] arguments) or absolute pathnames
pwalk(1)
Yadda yadda yadda yadda yadda yadda yadda yadda yadda yadda yadda yadda yadda yadda
Notes: Argument processing is primitive in places, but includes numerous sanity checks.
Contents of .xml or .ls files can be easily tailored in C, or other actions added for each leaf node found.
The code may have some obscure ‘hidden’ options that are not documented outside the code.

## Slide 10: pwalk Usage (1/3 - modes)
Primary modes (at most one of these may be specified) ...
  -ls // (*.ls) outputs list files, much like ‘ls –lR’
  -lsc // (*.ls) outputs list files, compact (inodes & names only)
  -lsd // (*.ls) outputs list directory summaries only
  -lsf // (*.ls) outputs list files with full pathnames
  -xml // (*.xml) outputs list files in XML format
  -cmp[=<options>] // (*.cmp) compare two presumably-similar file hierarchies
  -rm // (*.sh) outputs contain cd and rm commands[1][2]
  -trash // (*.sh) outputs contain cd and mv commands[1][2] [DEVELOPMENTAL]
  -csv[=<keyword_list>] // (*.csv) extract specific metadata fields into a .csv file [DEVELOPMENTAL]
  -audit (OneFS only) // (*.audit) report OneFS SmartLock file states in CSV format
  -fix_dates (OneFS only) // (*.fix) auto-correct damaged timestamps (with optional ‘-dryrun’ option)
Secondary modes (zero or more may be specified) ...
  +denist // Micro-benchmark: read first 128 bytes of every file encountered
  +tally // (pwalk_tally.csv) create CSV-formatted tally of files by age buckets
  +wacls (Linux only) // (‘Write ACLs’) convert POSIX ACLs to NFS4 ACLs and write to a pipe
  +xacls (Linux only) // (‘eXtract ACLs’) convert POSIX ACLs to NFS4 ACLs and write to a file
Notes: Modes that start with a ‘-’ are called ‘primary modes’, and they are all mutually-exclusive.
Modes that start with a ‘+’ are called ‘secondary modes’, and all or none of them can be specified.
Absent any primary or secondary modes, pwalk will exit with ‘nothing to do’.
[*] *.sh files with mv or rm/rmdir commands from –rm and –trash modes are not directory executable, but merely convey what pwalk did (or would do with –dryrun)
[2] with –dryrun option, no filesystem changes will be made

## Slide 11: pwalk Usage (2/3 – assorted options)
Generic options: all platforms ...
  -dop=<N> // Degree of Parallelism (N workers) // This option is what makes pwalk parallel!
  -gz // Compress primary mode outputs with gzip
  -output=<directory> // Specify where pwalk_YYYY-MM-DD_HH_MM_SS is created (default $CWD)
  -source=<directory> // Specify relative root for SOURCE directory arguments (default $CWD)
  -target=<directory> // Specify relative root for TARGET file hierarchy (for –cmp and certain other modes)
  -pfile=<file> // File containing extended arguments ([source], [target], [output], & more)
Miscellaneous options ...
  -bs=512 // interpret st_block_size units as 512 bytes rather than 1024
  -pmode // Exclude mode bits in output
  -q // Quiet mode (for -rm)
  -redact // Output hex-coded inode numbers rather than file names [*]
  +acls (Linux only?) // Include ‘+’ in mode bits output to indicate ACL present [**][***]
  +tstat // Include timing of stat() calls (for -ls, -xml)
Notes: [*] Causes more stat() calls to lookup inode numbers for all per-directory pathname components. Only done in for –ls?
[**] Causes an extra system call per-file unless on OneFS.
[***] Only for Linux POSIX-style ACLs

## Slide 12: pwalk Usage (3/3 – file selection options)
File selection options ...
  +span // Include directories that span filesystems (OFF by default)
  +.ifsvar[1] // Include .ifsvar directories (OFF by default)
  +.snapshot // Include .snapshot[s] directories (OFF by default)
  -select[2] // Select files with hardcoded selection criteria
  -select=lfn // Select files with > 255 bytes (<MAXFILE> [3]) in their names
  -[not]since=<ref_time>[4] // Select files with (mtime or ctime > mtime(<ref_time>))
  -[not]since_atime=<ref_time> // Select files with (atime > atime(<ref_time>))
  -[not]since_mtime=<ref_time> // Select files with (mtime > mtime(<ref_time>))
  -[not]since_ctime=<ref_time> // Select files with (ctime > ctime(<ref_time>))
  -[not]since_birth=<ref_time> // Select files with (birthtime > birthtime [5] (<ref_time>))
  -select=fake (OneFS only) // select only files with persisted IDs in the OneFS ‘fake’ range [DEVELOPMENTAL]
  -select=[no]stubs (OneFS only) // select only files which are -- or are not -- stubbed
NOTE: With +.snapshot – note that .snapshot[s] directories are not necessarily visible over SMB or NFS to begin with ... so this option may have no net effect in those circumstances.
Notes: [1] As of OneFS 9.0, /ifs/.ifsvar is not shown when the /ifs directory is traversed!
- Therefore, if /ifs/.ifsvar is to be included in a pwalk treewalk, it must be specified explicity and have this option specified!
[2] This is only for special cases where the pwalk code has been custom-modified for some specific tactical purpose
[3] pwalk’s ‘usage’ output will show the platform-dependent platform-dependent MAXFILE value, which is usually 1024
[4] For selection options using a <ref_time> ...
- integer values will be assumed to be Unix epoch-valued times, and non-integer values will be interpreted as an existing filename from which the pertinent timestamp is to be taken.
- <reftime> values are only evaluated to the second; microsecond and nanosecond values are not currently considered
- when the ‘’not” prefix is added, the selection uses less-than-or-equal logic complementary to the expressions shown above
- use ‘date –r’ and other date(1) options to convert to and from Unix epoch times. Google(Unix epoch time converter) for online time converters.
- NOTE: pwalk adjunct utility program ‘mytimes’ shows all file timestamps and flags in full detail
[5] birthtime is not available on all platforms, and may only be a copy of ctime in cases such as the Linux NFS client – so BEWARE

## Slide 13: pwalk Output Directory
pwalk always creates a pwalk-YYYY-mm-dd_hh_mm_ss/ directory with;
    pwalk.fifo – all directory paths processed (command-line args plus discovered directories)
    pwalk.log – progress log with timing and summary statistics
    workerNNN.<type>[.gz] – per-worker output file(s), where <type> is …
        .ls - with –ls, -lsc, -lsd, or -lsf
        .xml - with –xml
        .sh – with -rm
        .csv - with –csv
        .fix - with –fix_times
        .cmp - with –cmp[=<criteria>]
        .err – per-worker error file (only if errors occur)
        … plus possible secondary outputs …
        .acl4bin – for –xacls=acl4 outputs
        .acl4nfs - for –xacls=nfs outputs
        .acl4chex - for –xacls=chex outputs
    pwalk_tally.csv – only when the +tally secondary mode is used
    pwalk_audit.csv – only when the +audit secondary mode is used (OneFS only)
  NOTE: By default, user’s current working directory ($CWD) is where this directory is created, but that can be overridden with the –output=<directory> option or by using the [output] section of the –pfile=<file>
Notes: Contents of .xml files can be easily tailored, or other actions added for each leaf node found.
The code has some obscure ‘hidden’ options that are not documented outside the code.

## Slide 14: Path Arguments
Source - relative root for <directory> arguments
  Default: $CWD-relative
  Non-default: Specify the relative root for source <directory> arguments using the –source= option or by using the [source] section of the –pfile=<file>
  CAUTION: When set to a non-default value, <directory> arguments must be relative to the specified directory!
Target - relative root for –cmp= target hierarchy
  Default: N/A
  Non-default: Specify the relative root for the target file hierarchy using the –target= option or by using the [target] section of the –pfile=<file>
Output - directory in which pwalk output directory will be created
  Default: $CWD/pwalk-YYYY-mm-dd_hh_mm_ss
  Non-default: Specify alternative location for pwalk output directory creation by using the –output=<path> option or by using the [output] section in –pfile=<file>

## Slide 15: <directory> Arguments
<directory> arguments must consistently be either all-absolute or all-relative directory paths
relative directory paths …
  ... must be used whenever –source= or -target= options are used or whenever [target] or [source] directories are specified via –ipaths<file>
  default to being relative to the user’s current working directory ($CWD)
absolute directory paths …
  ... can only be used when no pwalk options are used to specify source or target relative root directories explicitly
Notes: This pseudo-code shows the key functions

## Slide 16: Multipathing with Multiple Equivalent Paths
Node 0
Node 1
Node 2
10.1.1.1
10.1.1.2
10.1.1.5
10.1.1.6
10.1.1.3
10.1.1.4
Multipath NAS Server: /ifs/data export or share accessible via multiple nodes and IP addresses
pwalk Client: access /ifs/data export or share mounted via multiple manually-mapped ‘equivalent paths’
# mount –t nfs –o ro 10.1.1.1:/ifs/data /mnt/1
# mount –t nfs –o ro 10.1.1.3:/ifs/data /mnt/2
# mount –t nfs –o ro 10.1.1.5:/ifs/data /mnt/3
------- ------ --------
‘Equivalent paths’ are conveyed to pwalk via the parameter file (–pfile=<file>) ...
# cat pfile
[source]
/mnt/1
/mnt/2
/mnt/3
pwalk gives same[1] results over NFS or SMB
It is recommended to use readonly mounts when only readonly operations are intended!
Notes: pwalk multi-pathing allows pwalk to ‘load balance’ across multiple target filesystem access paths for improved scaling.
In this diagram, the server is an abstracted Isilon cluster with 3 nodes and 6 possible network paths to the export or share.
Normally, the pwalk client will be a root-enabled client.
For safety sake, use readonly mounts when intending to do only readonly operations (ie: no –rm file write operations) from pwalk.
[1] ‘Same’ results except in rare cases where SMB provides different different timestamp precision or semantics.

## Slide 17: Multipathing – Source Example
# cat pwalk-paths
[source]
/mnt/1
/mnt/2
/mnt/3
# pwalk –dop=5 <mode(s)> –pfile=pwalk-paths <relative_directory_path> [<…>]
Worker 0 -> /mnt/1/<relative_directory_path>
Worker 1 -> /mnt/2/<relative_directory_path>
Worker 2 -> /mnt/3/<relative_directory_path>
Worker 3 -> /mnt/1/<relative_directory_path>
Worker 4 -> /mnt/2/<relative_directory_path>
-pfile= [source] format is one path-per-line, with ^[%#*] lines ignored as comments
All equivalent [source] paths must exist and represent the same actual directory
All source pathnames will be evaluated relative to the [source] paths
When [source] is defined, the –source= option cannot be specified
Source root paths will be bound to absolute paths, with all symlinks fully-resolved
Notes: Multipathing logic was rewritten in pwalk 2.04 to allow both source and target multi-pathing. (See next slide.)
Equivalent source paths are best thought of as ‘equivalent relative root paths’, which is the point relative to which pwalk directory arguments are evaluated.
Expanding on that, keep these three perspectives in mind;
  With multipathing, pwalk <directory> arguments must be relative, as represented here by <relative_directory_path>.
  With multipathing, these equivalent ’relative root source paths’ are where ‘.’ is considered to be.
  With multipathing, <directory> command-line arguments cannot be absolute – i.e. cannot begin with a ‘/’.
  With multipathing, -source= cannot be used because it would be contradictory.
Step-by-step, using this feature looks something like;
  Create the /mnt/[123...] directories local to the pwalk client
  Mount the same export/share to each of /mnt/[123...] – manually managing the IPs from which the export/share is accessed.
    One will usually wish to make the pwalk client a root client of the source directory hierarchy!
    One might usually prefer to make these mounts READONLY (-o ro).
    CAVEAT USER! Placing an excessive load on a production node in a cluster can be a Bad Thing. Be careful!
  pwalk ... –pfile=<pfile> - where the ‘equivalent (relative root) paths’ are specifed in the [source] part of the <pfile>.
  pwalk ... –dop=<N> - distributes multiple workers across the ‘equivalent (relative root) paths’.
    <N> will typically be chosen to be a multiple of the number of ‘equivalent source root paths.
    Each worker’s outputs will reflect the actual mount path it used.

## Slide 18: Multipathing – Source & Target Example
# cat pwalk-paths
[source]
/mnt/1
/mnt/2
/mnt/3
[target]
/mnt/target1
/mnt/target2
# pwalk –dop=5 <mode(s)> –pfile=pwalk-paths <relative_directory_path> [<…>]
Worker 0 -> /mnt/1/<relative_directory_path> /mnt/target1/<relative_directory_path>
Worker 1 -> /mnt/2/<relative_directory_path> /mnt/target2/<relative_directory_path>
Worker 2 -> /mnt/3/<relative_directory_path> /mnt/target1/<relative_directory_path>
Worker 3 -> /mnt/1/<relative_directory_path> /mnt/target2/<relative_directory_path>
Worker 4 -> /mnt/2/<relative_directory_path> /mnt/target1/<relative_directory_path>
-pfile= [source] and [target] format is one path-per-line, with ^[%#*] lines ignored as comments
All equivalent [source] or [target] paths must exist and represent the same actual directory
All source pathnames will be evaluated relative to the –source= or [source] relative roots
All target pathnames will be evaluated relative to the –target= or [target] relative roots
When [source] or [target] paths are defined, –source= or –target= options cannot be specified
Source and target root paths will be bound to absolute paths, with all symlinks fully-resolved
Notes: [source] and [target] paths are independently specifiable. (Since pwalk version 2.04)

## Slide 19: pwalk Generic Modes

## Slide 20: -ls, -lsc, -lsc, & -lsf primary modes
pwalk -ls ... – (basic) much like ‘ls –l’
@ usr
drwxr-xr-x 980 0 bin
drwxr-xr-x 294 0 lib
lrwxr-xr-x 1 8 X11
…
drwxr-xr-x 47 0 share
S: f=0 d=7 s=1 o=1 errs=0 space=0 size=328
pwalk -lsc ... – (compact) with filenames only (skips directories)
@ usr
l X11
S: f=0 d=7 s=1 o=1 errs=0 space=0 size=328
pwalk -lsd ... – (directories only) like –ls, but show only directory totals
@ usr
S: f=0 d=7 s=1 o=1 errs=0 space=0 size=328
pwalk -lsf ... – (full pathname) like –lsc, but full (or relative) path for each file
@ usr
d usr/bin
d usr/lib
l usr/X11
…
d usr/share
S: f=0 d=7 s=1 o=1 errs=0 space=0 size=328
Notes: -ls with +acls will show a ‘+’ where an actual ACL is present (platform-dependent)
The ‘pwalk_ls_cat’ program is a simple UNIX-style filter which will transform –ls_special output into a stream of fully-qualified pathnames.

## Slide 21: -xml primary mode
pwalk -xml ... – much like ‘-ls’ output, but in primitive XML format
OUTPUTS: worker<nnn>.xml[.gz] files
Notes: -ls with +acls will show a ‘+’ where an actual ACL is present (platform-dependent)
The ‘pwalk_ls_cat’ program is a simple UNIX-style filter which will transform –ls_special output into a stream of fully-qualified pathnames.

## Slide 22: -rm primary mode – data destructive!
pwalk –rm …
  only removes files, symlinks, and other non-directories -- never directories
  works with –dryrun to suppress any live changes
  a count of files removed will be shown in the pwalk.log file
  WARNING: Without ‘-select’, all files in the treewalk will be deleted!
OUTPUTS: worker<nnn>.sh[.gz] files, which have three columns;
  Column 1: ‘@’ to show directory in which files are deleted, or <N> to show error code from trying to remove the file (or ‘#’ in –dryrun mode)
  Column 2: ‘cd’ for directories, or ‘rm’ for files selected to be removed
  Column 3: filename, enclosed in double-quotes
  NOTE: These .sh outputs are just a record of what pwalk did; they are not directly executable!
WARNING: Make sure that pwalk’s output files do not get deleted!
  Use of the –output=<directory> option is highly-recommended with –rm to place the outputs out of harm’s way!
Notes: Use with extreme care!

## Slide 23: -cmp[=<options>] primary mode (1/3)
pwalk –cmp[=<options>] - performs a one-way comparison between two presumably-similar file hierarchies; a SOURCE tree and a TARGET tree
  For each file and directory in SOURCE tree, the status of the corresponding file or directory in the TARGET is reported according to the comparison criteria conveyed by the given <options>
  At a minimum, pwalk will always report if the TARGET file or directory does not exist or does not have the same type as the SOURCE file or directory, but <options> can be given to expand the comparison to include owner, group, file size, and other factors as shown on the next slide
  NOTE: The ‘one-way’ nature of the –cmp analysis means that TARGET files which are not present in the SOURCE hierarchy will not be reported!
OUTPUTS: worker<nnn>.cmp[.gz] files, with three columns of content as follows;
  Column 1: ‘@’ for directory being scanned, ‘d’ for directory found during scan, ‘-’ for ordinary file, ‘s’ for symlink, ‘p’ for pipe, ‘c’ for character special, ‘b’ for block special, ‘?’ for other type
  Column 2: a character string expressing all of the detected differences between the SOURCE and TARGET, per the letter codes shown on the next slide
  Column 3: the directory or filename entry that was compared

## Slide 24: -cmp[=<options>] primary mode (2/3)
Notes: Keywords can be combined in a comma-delimited list as arguments to –cmp= -- but E, T, and ! results are always reported.
Code letters shown in column 2 of are used to indicate differences between SOURCE and TARGET files in pwalk .cmp outputs.

## Slide 25: -cmp[=<options>] primary mode (3/3)
Examples ...
pwalk –cmp …
  Reports differences in existence (E) and file type (T).
pwalk -cmp=size,mtime …
  Reports differences in existence (E), file type (T), file size (s), and file mtime (m).
pwalk -cmp=size,content …
  Reports differences in existence (E), file type (T), file size (s), and contents (C). Contents will be shown to differ whenever SOURCE and TARGET files differ in size, but when the files have the same size, an exhaustive bytewise comparison of the files will be performed (which is very bandwidth- and runtime-expensive).
Notes: This set of pwalk functionality is documented in the cited paper; “Converting POSIX ACLs to NFSv4 ACLs with pwalk(1)“
As ‘+’ secondary modes, these can be specified independently of the primary mode used.
The OneFS-specific binary ‘wacls’ is not made widely-distributed, and is not end-user buildable.

## Slide 26: +tally secondary mode
pwalk ... +tally ... - creates a cross-sectional summary report of file counts and space usage by file size
  This logic is currently hard-coded, but can be easily modified to use different “Bucket” thresholds. It should be externally parameterized version in a later version, ideally by using a [tally] section in the parameter file.
OUTPUTS: a single pwalk_tally.csv file with these columns;
  “Tag” – default is ‘pwalk’, settable with optional <tag> using +tally[=<tag>]
  “Bucket” – file size threshold
  “Files” – file count
  “Files%” – … as percent of total file count
  “Size” – total nominal bytes
  “Size%” – … as percent of total file sizes
  “Space” – total allocated bytes – includes protection overhead
  “Space%” - … as percent of total space used
NOTE: No output will be generated unless pwalk runs to a successful completion!
Notes: This pseudo-code shows the key functions

## Slide 27: +denist secondary mode
pwalk ... +denist ... – causes pwalk to do a readonly open() of every file and read the first 512 bytes of every file.
This is a micro-benchmark for the I/O aspect of what is known as ‘de-NISTing’ in the world of eDiscovery and litigation support (https://www.google.com/search?q=de-nisting)
NOTE: This will impact the filesystem access times for every file examined whenever access time tracking is enabled!
NOTE: No output will be generated unless pwalk runs to a successful completion!
OUTPUTS: Summary statistics of bytes read in the pwalk.log file.
Notes: This pseudo-code shows the key functions

## Slide 28: pwalk Platform-specific Modes

## Slide 29: OneFS-native pwalk Caveats!
Running any binaries natively on OneFS which are not part of the official OneFS release is completely unsupported by Isilon. Refer to the DISCLAIMERS in these slides and the source code.
If you are not traversing very large hierarchies, it may be better to simply use standard single-threaded tools like ‘find /ifs/data/Isilon_Support/pkg -ls | gzip’ or ‘ls -lR /ifs/data/Isilon_Support/pkg | gzip’.
The bin/onefs7 binaries are no longer maintained, but the bin/onefs8 binaries might work on OneFS 7. The difference between the two binaries is the APIs they use and the tools with which they are built – not their runtime binary compatibility … at least in principle. Between OneFS 7 and OneFS 8, Isilon switched from using gcc to using clang (https://clang.llvm.org/comparison.html). Native OneFS 7 builds and runs have not been tested for some time, but if you have a real need for it, please contact the author to discuss.
Be sure that your pwalk output is not on a OneFS system disk! Otherwise, your output files might fill up a system disk and lead to serious operational issues! It is best to cd somewhere in /ifs before running pwalk, but the -output=<directory> path is another option.
Unlike native OneFS utilities, pwalk does not distribute its workload across nodes per se. All worker threads will run on the specific node on which pwalk is initiated. Since -dop=8 may drive up to 80% CPU on many node types, it is wise to experiment to determine how much concurrency is prudent to prevent an excessive competitive impact on production workloads.
The multi-pathing option ([source] …) is not available in the OneFS version.
The simplest way to install the binaries you want to use on OneFS is to copy them into /usr/local/bin on the particular node(s) where you will use them. For example, ‘cp bin/onefs8/pwalk /usr/local/bin’. Note that no executables can be run directly from anywhere in /ifs, because /ifs is always mounted as ‘noexec’ on OneFS. Alternately, one might keep the binaries someplace like /root/pwalk/<version>/bin/onefs8/…’ and symlink them from /usr/local/bin to make the versions clear and allow switching between versions just by changing the symlinks.
OneFS-native pwalk binaries are not end-user buildable. Please contact the author if you have requirements for non-standard OneFS-native pwalk functionality.

## Slide 30: OneFS-only: –audit primary mode
PROBLEM: isi worm file view <file>
  Only examines one file at a time – not viable at-scale!
  Output has history of bugs in Compliance Mode
  No consideration of ‘latent commit’ state – when a non-committed file is pending commit on the next access
Questions, questions, questions;
  Which files are COMMITTED?
  Which files are readonly, non-deletable? (Includes COMMITED, EXPIRED, and ‘latent commit’ files!)
  Which files are not COMMITTED?
  Which files are EXPIRED?
  How much space can be freed by deleting EXPIRED files?
  When will files expire, assuming autocommit occurs?
  Which files have manually-set retention dates?
  How to create a script to adjust retention dates for selected files?
  How to create a script to bulk delete expired files?

## Slide 31: OneFS-only: –audit primary mode
Produces CSV-formatted .audit outputs for all files which shows all file timestamp values, plus OneFS WORM state metadata and certain derived ‘ephemeral’ values for files in OneFS SmartLock domains
A map of the CSV column definitions is written to pwalk.log
Restrictions
  MUST run natively on OneFS
  Requires pwalk_python.py to be present in directory from which pwalk is invoked
  NOTE: Invoke pwalk by its full explicit pathname to help it find its Python file
    e.g.: /usr/local/bin/pwalk …

## Slide 32: OneFS-only: -fix_times primary mode
Esoteric limited-use functionality! Not for general-purpose use! Details only appear in Dell EMC-internal-only blog posting.
Implemented in pwalk 1.91
Due to limitations with timestamp handling over SMB or NFS4, this must generally be run natively on OneFS for correct results!
Notes: This pseudo-code shows the key functions

## Slide 33: OneFS-only: POSIX ACL Migration from Linux
‘wacls’ – Write ACLs utility
  This setuid-root program runs natively on OneFS as a symbiont to pwalk’s Linux-only POSIX ACL migration features (see next slide)
  Errors and messages are logged to /ifs/wacls/wacls.<pid>
    NOTE: The /ifs/wacls directory must be pre-created before using wacls!
  -cd=<pathname> option allows setting initial path in /ifs appropriate to interpreting the relative pathnames from the input stream of [NFS4 binary ACL, pathname] tuples
Notes: The NFS4 binary ACL format and the [NFS4 binary ACL, pathname] tuple formats are unique to pwalk.
The main distinction between the standard NFS4 ACL format and pwalk’s binary format is that pwalk uses only binary UID and GID trustee values rather than UTF-8 strings.

## Slide 34: Linux-only: POSIX ACL Migration to OneFS
Migration of POSIX ACLs to OneFS …
  On Linux, POSIX ACLs (ACL+DACL) are extracted for each file or directory
  The POSIX ACLs are translated to NFSv4 ACLs (skipping trivial[*] ACLs) using the algorithm, described in https://tools.ietf.org/html/draft-ietf-nfsv4-acl-mapping-05 (“Mapping Between NFSv4 and Posix Draft ACLs”)
  Only numeric UID and GID IDs are used (no name translations are applied)
+wacls=<command> // ‘Write ACLs’ – secondary mode
  Binary [NFSv4 ACL, pathname] tuples will be piped to the specified command; normally a remote invocation of the OneFS-native pwalk symbiont called ‘wacls’
    OneFS-native ‘wacls’ binary runs with root privilege to apply the NFSv4 ACL values
+xacls=[bin|nfs|chex] // ‘eXtract ACLs’ – secondary mode
  For all non-trivial POSIX ACLs found, translate them to NFS4 ACLs to binary, nfs4_setfacl, or CHEX format in <workerNN>. [acl4bin|acl4nfs|acl4chex] output files
This complex functionality is more-fully described in the document “Converting POSIX ACLs to NFSv4 ACLs with pwalk(1)“, included in this bundle as doc/pwalk_acls.docx
Notes: [*] A ‘trivial’ ACL is one that can be accurately represented using POSIX mode bits only.
As ‘+’ secondary modes, these can be specified independently of the primary mode used.

## Slide 35: pwalk Option Footnotes

## Slide 36: -dop=<N>
‘Degree of Parallelism’ (number of worker threads) - This is the MAIN OPTION that makes pwalk ‘parallel’!
Default is 1, maximum is 128.
When multi-pathing is used, the number of workers per-node will be (NUMBER_OF_PATHS/<N>).
BEWARE: 8 workers per node will drive many Isilon nodes to 80% CPU utilization! Choose a value that will not cause pwalk to compete excessively with production workloads!

## Slide 37: -gz
gzip primary pwalk outputs.
This is a real space-saver for directory hierarchies large enough to warrant using pwalk in the first place.
NOTE: pwalk uses large buffers to communicate with gzip, so compressed output files will tend to grow s-l-o-w-l-y ...

## Slide 38: Operational Notes

## Slide 39: pwalk Usage Notes
pwalk is best run as the root user from a NAS client that has been specified as a root client for the export(s)/share(s) being scanned
  This avoids permissions problems in traversing directories
  Running directly on OneFS is possible, but slower than running from a NAS client
  Note that pwalk is agnostic of the filesystem type being scanned. Local filesystems, NFS exports, and even SMB shares can be scanned – but the optimal concurrency can vary greatly between use cases.
CAUTION: treewalks with high per-node-concurrency can have a significant impact on OneFS initiator nodes, especially in CPU usage!
  Test pwalk at lower concurrency levels (2 to 4) to assess how much pwalk competition your cluster’s production workload can tolerate
  pwalk’s CPU-per-worker impact on a OneFS node should scale more-or-less linearly
The -paths= feature is recommended to spread pwalk’s impact across OneFS cluster nodes
  Multiple readonly mounts are recommended
  With NFS, be sure that READIRPLUS is enabled for all mounts
In the unlikely event of a uncaught fatal error in pwalk, it is best to have core dumps enabled to facilitate diagnosis (eg: use ulimit –c unlimited on Linux prior to pwalk operation)
  core.<pid> is the standard Linux core file destination, but it is configurable
  Released versions of pwalk have not been known to dump core under any circumstances, but if it happens, please report it!
Notes: This pseudo-code shows the key functions

## Slide 40: About NFS READDIRPLUS
If every lstat(2) call had to traverse a NAS protocol, network latency would cause it to take a long time to obtain information about a large number of files.
NFSv3 can use its READDIRPLUS RPC to include file metadata with each call.
NFSv4 does not have a READDIRPLUS RPC per se, but uses a variable attribute mask to obtain similar results.
Most NFS clients honor the ‘rdirplus’ mount option for both NFSv3 and NFSv4 mounts as hint to fetch metadata in batches.
In Linux, ‘mountstats <mount_point>‘ is handy for seeing what RPCs are generated, along with their service times.

## Slide 41: Size matters! Budget output space!
Incremental Per-File Output Bytes (PFOBs) add up …
  One million (10^6) files -> 1 MB PFOB
  One billion (10^9) files -> 1 GB PFOB
With –gz, estimate 3x to 4x compression
  EXAMPLE: 1 billion files @ 128 bytes-per-file
  ~128 GB estimated output, compressed to ~42 to 34 GB
With –ls, the –pmode option reduces output size by omitting file mode column
The –lsc primary mode is explictly designed to minimize output space
With –csv, one can specify only the metadata columns desired
Since pwalk source code is FREE, one can edit the code to only output the minimal information required for a specific purpose
Notes: For large filesystem scans, budget output space accordingly!

## Slide 42: Performance: YMMV
Test Directory Structure: ~32 millions files including ~64 thousand directories
Target cluster: 3-node 5400S with no SSD running OneFS 7.1.0
Linux client: Centos 6 on 3-core NNN GHz AMD processor
  Single 1 GbE switched network link to cluster
  Single 7200 RPM SATA disk with EXT3 filesystem used for output
Output size; ~1.8 GB uncompressed, 160 MB compressed
-dop= | paths | seconds | files/sec | files/sec/path | 
1 | 1 | 11430 | 2788 | 2788 | 
2 | 1 | 5832 | 5464 | 5464 | 
4 | 1 | 2901 | 10985 | 10985 | 
8 | 1 | 2491 | 12794 | 12794 | 
10 | 1 | 2388 | 13346 | 13346 | 
16 | 1 | 2359 | 13512 | 13512 | <- diminishing returns
18 | 3 | 1218 | 26174 | 8725 | 
24 | 3 | 1145 | 27834 | 9278 | 
30 | 3 | 1136 | 28044 | 9348 | 
24 -gz | 3 | 1114 | 28609 | 9536 | <- slight GAIN with –gz!
48 | 3 | 1120 | 28455 | 9485 | <- diminishing returns
Notes: This example does not represent the limits of pwalk throughput; merely the results of some tests that were run.
One should also characterize the network bandwidth and CPU usage on both the client and the target storage to find the right tradeoff between performance and resource saturation.

## Slide 43: Performance Factors
Client …
  Mount options (esp. ‘rdirplus’, ‘acdirmin’, ‘acdirmax’)
  Use of –paths= multi-pathing
  TCP/IP, RPC, and NIC tunables
Network …
  Bandwidth
  Latency
  Congestion
Server …
  CPU power
  OneFS version
  OneFS SSD usage for metadata (metadata-read, metadata-write, L3)
  Parameters per RDIRPLUS operation (export option)

## Slide 44: Open Files Limit
Per-worker -> (8*N_WORKERS) max
  #N_WORKERS - READONLY file open
  #N_WORKERS – Primary output (.ls, .xml, .audit, .cmp, .fix, .out)
  #N_WORKERS – Python pipe (w/ -audit)
  #N_WORKERS - .err file (only if worker generates errors)
  #4*N_WORKERS – ACL outputs (including –wacls= pipe)
Per-process (6 + N_SOURCE_PATHS + N_TARGET_PATHS)
  #N_SOURCE_PATHS + #N_TARGET_PATHS - SOURCE and TARGET paths
  #1 - .log file
  #2 - .fifo (push and pop handles)
  #3 - stdin, stdout, stderr
Transient
  #1 – pwalk_tally.csv
  #1 - -paths=

## Slide 45: Platform-specific Limitations
OSX / macOS
  /dev/fd/<n> entries that look like directories cannot be opened with opendir(), and will therefore produce errors

## Slide 46: Footnotes
Only directory pathnames are allowed on the command line
Worker wakeups per run are non-deterministic, and may vary between runs
Platform-specific summary statistics vary widely in content and accuracy; take them with a grain of salt
pwalk’s space accounting is not precise …
  Files with multiple hard links will have their space usage redundantly counted by pwalk
  pwalk <path> entries include directory space usage, but <file> entries for all directories are shown as 0 bytes allocated and 0 bytes used (to avoid double-counting)
  pwalk <file> entries for symlinks will report zero-length space allocation (but should probably at least report the space required for their inode allocations)

## Slide 47
Q & A?

## Slide 48: Extensions and Refinements

## Slide 49: pwalk via PAPI (FUTURE)
Enumerating directories via HTTP GET operations is less transactional, therefore less latency-sensitive, and therefore potentially MUCH faster!
Notes: This pseudo-code shows the key functions

## Slide 50: pwalk –find mode (FUTURE)
FUTURE: Scalable subset of find(1)
Notes: This pseudo-code shows the key functions

## Slide 51: pwalk +verify Mode (FUTURE)
For files types whose validity can be determined by inspection, perform the requisite test
  GZIP - .gz, .tgz – test with gzip –tq
  === MORE TBD ===
    .c, .txt, .asc, .info – check for all ASCII
Notes: This pseudo-code shows the key functions

## Slide 52: pwalk.c - Version 1.x
Simple FIFO-based scanning of directories
  if the last directories that get popped are very large, their worker threads may end up being laggards
Optional load-balancing
  ‘-paths=<pathfile>’ – spread load across multiple mount points that point to the same directory hierarchy
  Concurrent RDIRPLUS workloads can be quite compute-intensive for a OneFS initiator node
Portable code using pThreads library
  worker threads do all the work
  no exec/spawn overhead
  coding strategy restricted by threaded worker context
    for example, chdir(2) cannot be used, because it is process-global, and would effect all threads

## Slide 53: Change the FIFO to a Heap?
What if the last directory scanned is unusually large and takes a long time to process?
  High percent of total elapsed time could be waiting on last worker
  Changing the FIFO to a heap and always popping the next biggest directory might mitigate this
    Heap approach is no guarantee though; largest directory might be encountered while scanning a very small directory
  Current code that logs worker wakeups allows observing, for example, if significant periods of time pass with less than all <N> workers being busy

## Slide 54: Keep Track of Hard-Linked Files?
pwalk could log all files with a link count greater than one to correct for redundantly-counted space at the end of a run
  A file’s inode number uniquely maps to the space it uses

## Slide 55: Optionally, Pre-Warm OneFS L2
There might be some benefit in pre-reading large directories using large reads to warm-up the OneFS L2 cache; notionally, something like …
  dd if=<directory_name> bs=64k of=/dev/null

## Slide 56: Have Workers Do More Work
Uses cases abound …
  PowerCopy
  PowerChmod
  PowerGrep
  PowerPurge – pwalk –rm –select=<…>
  PowerScan – pwalk -xml
  PowerCmp – pwalk –cmp –source=<…> -target=<…>
  PowerPermissionsRepair

## Slide 57: Use Per-Worker Slave Processes
Possible Motivations …
  Cannot change working directory in a thread; current-working-directory is a process-global thing
  Optimal per-worker performance may require more memory per worker than will fit well in threaded model
  Per-process open file count or other limits could limit maximum thread count or the complexity of the work done by worker threads
  Might want to distribute work using rsh of some other means to leverage multiple clients
Implementation …
  Not too hard to popen() subordinate processes

## Slide 58: Implementation Notes

## Slide 59: Tools Matrix
Program | OneFS | Linux | OSX | Solaris
pwalk – PowerWalk[1] | ✓ | ✓ | ✓ | ✓
touch3 – Set atime, mtime, & birthtime[2] | ✓ | ✓ | ✓ | ✓
mystat – stat(1)++ w/ full precision | ✓ | ✓ | ✓ | ✓
hacls – Hexify ACLs (produce CHEX format) | ✓ | ✓ | ✓ | ✓
chexcmp – Compare CHEX-formatted ACEs | ✓ | ✓ | ✓ | ✓
wstat – WORM stat | ✓ |  |  | 
wacls – Write ACLs (setuid root) | ✓ |  |  | 
pwalk_python.py – Co-process for -audit | ✓ |  |  | 
xacls – eXtract & translate POSIX ACLs |  | ✓ |  | 
[1] Features vary by platform
[2] birthtime not available on all platforms
Notes: This a very straightforward C code, with the only consideration being inclusion of the pThreads library (the POSIX portable threads library).
The O’Reilly book is all one needs to get started.

## Slide 60: stat(2) – syscall - per-file metadata
fstat(), lstat(), stat(), fstatat() calls return info like this about a file …
struct stat { /* when _DARWIN_FEATURE_64_BIT_INODE is defined */
dev_t st_dev; /* ID of device containing file */
mode_t st_mode; /* Mode of file (see below) */ [1] e.g.: rwxr-xr--
nlink_t st_nlink; /* Number of hard links */
ino_t st_ino /* File serial number */ i.e.: inode #
uid_t st_uid; /* User ID of the file */
gid_t st_gid; /* Group ID of the file */
dev_t st_rdev; /* Device ID */
struct timespec st_atimespec; /* time of last access */
struct timespec st_mtimespec; /* time of last data modification */
struct timespec st_ctimespec; /* time of last status change */
struct timespec st_birthtimespec; /* time of file creation(birth) */ [2]
off_t st_size; /* file size, in bytes */ ‘nominal’ size (bytes)
blkcnt_t st_blocks; /* blocks allocated for file */ [3] ‘allocated’ (~raw) size (sectors|kb)
uint32_t st_flags; /* user defined flags for file */
uint32_t st_gen; /* file generation number */
int32_t st_lspare; /* RESERVED: DO NOT USE! */
int64_t st_qspare[2]; /* RESERVED: DO NOT USE! */
};
[1] When an ACL is present, the mode bits are a OneFS approximation of the ACL.
[2] Not all filesystems store ‘birth time’ or provide for it in their stat(2) implementation; NFSv3 cannot convey it, and not all NFSv4 clients handle it correctly; it may be presented as either ‘not available’ or as a blind copy of the ctime.
[3] Modern NFS servers may return a number of 1024-byte units rather than 512-byte units. From OneFS, this value includes the data protection overhead of a file. The ratio of st_blocks to st_size will depend on each files’s actual protection strategy (mirrored or FEC parity) and may vary with the size of the OneFS node pool containing the file.
Notes: Gathering and presenting this data is what pwalk does. This example is from OSX, but the structure is very similar between various implementations.
OneFS normally foregoes the metadata-maintenance expense of keeping access times accurately. Their updating frequency is adjustable, but typically no more aggressive than once-per-day
http://pubs.opengroup.org/onlinepubs/009695399/basedefs/sys/stat.h.html – “The unit for the st_blocks member of the stat structure is not defined within IEEE Std 1003.1-2001. In some implementations it is 512 bytes. It may differ on a file system basis.”

## Slide 61: directory_scan() Pseudo-code
// For every directory popped from FIFO …
opendir(directory)
stat(directory)
process_entry(‘start’, directory)
while (readdir_r(...)) {
stat(entry)
if (S_IFDIR(entry)) fifo_push(entry)
else collect_statistics(entry)
process_entry(‘entry’, entry)
}
process_entry(‘end’, directory)
closedir(directory)

## Slide 62: Threads vs. Processes
 | Processes | Threads
Control | Shells & shell scripts Dispatchers/Listeners Any program (system()) | Compiled code (usually)
Synchronization | Filesystem objects Inter-Process Communication (IPC) | Lock-protected memory in the containing process’s address space
Complexity & Versatility | Awkward or expensive to implement complex logic | Extreme versatility and access to OS, but requires skills and compiler step
Monitoring (Solaris) | PID (prstat –m) | LWPID (prstat –mL)

## Slide 63: Per-Worker Memory Usage
Usage | Space (KB)
Wlog output buffer | 32
Filename scratch space | 1 to 8 KB (depends on OS)
stat() buffer | 1 to 8 KB (depends on OS)
… | …
It adds up at high worker count …
Summary stats in pwalk.log give actual usage